## Slide 1: Tarek Haddad MEDTRONIC
Discount Prior method (DP)

## Slide 2: Bayesian method with informative prior
If suitable prior is available 
  Efficient use of information
  Better precision in estimate
  Smaller and faster trials
    Fewer people exposed to trials
    Helps patients get latest medicine/devices faster

## Slide 3: Can we help make informative priors trail more common
Bayesian approach | Good Operating characteristics | Easy to explain and implement | Computational burden | Applicable to many types of trials
Hierarchical model | Sort of | Sort of | No | Sort of
Commensurate prior | No | No | No | Yes
Fixed power prior | No | Yes | Yes | Yes
New method? | Yes | Yes | Yes | Yes
Can we do better?
Very few Bayesian informative prior trials conducted
Some challenges with current methods
No method appeared to meet all the needs
Fixed power prior is very good, but lacks good operating characteristics
Notes: Hyper priors are hard

## Slide 4: Fixed Power prior
Very easy to explain and implement!
a priori set weight of prior using ( between 0 and 1)
  No weight=0
  full weight =1
  Set weight based on baseline patient characteristics and clinical and device similarities between the two studies
Borrowing is not dynamic:
If similarity assumption of prior is incorrect there is no way to mitigate
Can be very problematic at the end of trial
Sensitivity analysis can show the prior and current data are statistically different yet we still borrowed heavily
Unjustifiable bias in estimate

## Slide 5: Add a penalty to power prior?
Can we leverage the power prior approach but improve its operating characteristics?
  A fixed power prior with a penalty function applied
    Still go through the same work you would do with baseline characteristics and clinical similarities between the two studies
  Penalty function is a pre-specified decision rule
  Penalty function allows borrowing if original prior assumption is justified
  Controlling operating characteristics
  Is easy and understandable to both clinicians and statisticians

## Slide 6: Power prior simple fix
Specify a fixed prior; if there is a statistically significant difference, discount the prior data 100%
  Problematic  causes dramatic changes in degrees of freedom on an arbitrary point
  P-value = 0.099  discount 100%
  P-value = 0.10  discount 0%
If the p-values varies only slightly, the prior data should receive only slightly lower weight, not zero weight!

## Slide 7: Discount function
Create a more continuous and gradual penalty
As the confidence in prior and current data similarity decreases so does your weight given to the prior

## Slide 8: Discount Prior procedure
Compare historical and current data (poolability test)
Discount (strength of historical data) using discount function to obtain
Combine historical and current data using power prior () and Estimate from posterior
historical data
current data
a
Estimate
Start with traditional fix power prior; determine max weight using clinical judgement

## Slide 9: Discount prior interpretation
Discount prior is a procedure not a statistical model
is not parameter in a traditional sense
It is a penalty on  = W*
  Where W is the penalty and goes from 0 to 1
Discount function is very conservative approach
You need to demonstrate your initial assumption of similarity is justified
In the end this a fix power prior, but we have an added a layer of protection

## Slide 10: Adaptive study designs with DP
Take sequential looks at data as trial progress
Adaptive sample size
At interim looks apply discount function and imputation methods
If current ≠ historical than 0, need to enroll more current patients
  Converts to traditional adaptive design
  or call Futility
If current = historical than 
  Stop enrollment early (expected success)

## Slide 11: Similar to an Adaptive Sample size re-estimation Bayesian trial
Adaptive trial procedure:
  Make an assumption of the treatment effect size
  At Interim looks you observe the current data to assess original assumption of effect size,
  based on the pre-specified decisions rules do you enroll more subjects or stop enrollment.
  Perform simulations to assess operating characteristics effects, both negatives and benefits of the multiple looks at the current data
Discount Prior procedure:
  Make an assumption of the similarity between prior the current
  Observe the current data and assess original assumption of similarity,
  based on the pre-specified decisions rules (discount function) do you discount prior and enroll more subjects or stop enrollment
  Perform simulations to assess operating characteristics effects both negatives and benefits of the additional look at the current data

## Slide 12: Power prior: Combining historical data with new patients
likelihood function of the historical data
Power prior:
goes from 0 to 1
Down weight the effect of from to
How to determent ?

## Slide 13: Agreement measure
We develop a measure of agreement, between the historical data and the current data
Assume is historical data and y is current data
Develop the pre-posterior distribution new data and historical data, respectively, where both with minimally informative priors.
(1)
(2)
Let denote an estimate of based on the historical data alone
The variable is an estimate of using either the current data alone
and are nuisance parameters

## Slide 14: Agreement measure
where is the standard normal CDF, and and are variance estimates of the per-posterior distribution of and
construct a z-score from each set of draws from (1) and (2)
(3)
Accounting for uncertainty in Agreement measure and
You get a distribution for and

## Slide 15: Discount Function
Apply the discount function
= W(a)*
If W is the identity function
= a*
identity function

## Slide 16: Four models were compared
Models
  Discount prior (DP) identity function (= a)
  Discount prior(DP) Weibull(2,0.6)
  Discount prior (DP) Weibull(1,0.5)
  Hierarchical model
  Commensurate prior
  chosen to minimize the DIC (Ibrahim, Chen, Gwon, & Chen, 2015)
Metrics
  Bias
  Type I error
  Mean squared error (MSE)
  Power

## Slide 17: Simulation set up
Normal distribution historical data sets with and =1 and sample size of .
Small sample size (=N=25) was used to exacerbate any negative behaviors that would be observed under small sample sizes (For example DP and DIC look at the data twice)
We simulated 20,000 data sets per point from a normal distribution with a mean , standard deviation of 1, and
To examine the effect the prior data has on the estimation and inference of the posterior of , we selected true value, from the range -3 to 3 ( range of the prior distribution)
All model can have the same Maximum weight (=25)
was Accepted at a 0.975 posterior probability level for all models (error rate 0.025)

## Slide 18: Desirable properties
See some effects of prior in an agreement region
Minimal effects of prior in discordant region

## Slide 19: Bias
Bias is defined as the posterior mean minus True mean .
For values of near zero, historical data has influence on the posterior mean resulting in small bias for all models.
As moves away from the historical mean of zero, there is an initial spike in bias and then a shrinkage towards zero.
The mean bias of the DP methods is nearly zero when the true value of is greater than 1.5.
Meanwhile, the other models have increased bias even for significantly different (pvalue<0.001) between current and historical data.
statistically different (pvalue<0.001) and bias in positive direction treatment effect size looks better then current data alone: This is very hard to defend!
Discordant regions
Discordant regions

## Slide 20: Type I error rate
The type I error is computed under the following hypothesis test vs. , where =-3 to 0
For the DP methods, the type I error rate is estimated near the nominal value of 0.025 for values of
The hierarchical and commensurate, have inflated type I errors suggesting that these methods allow the historical data to have influence even in the presence of a significant difference (pvalue<0.001) between the current and historical data
The DP with identity has a similar type 1 error Peak as hierarchical, however it reduces faster and eventually hits nominal type 1 error of 0.025
Discordant regions

## Slide 21: Inflating your posterior probability acceptance criteria
In other Bayesian methods, it is common to inflate posterior probability acceptance criteria to maintain type I error rate:
  E.g. Require Pr(Ө>x) > 0.99 vs. 0.975 to maintain type I error under 0.05
This is confusing and defeats the purpose of using Bayesian methods to produce simple probability statements.
No way to mitigate the bias (or MSE) problems with the other methods
  E.g. statistically different (pvalue<0.001) and bias is high in positive direction treatment effect size looks better then current data alone This is very hard to defend!!
Using DP Bias will be very small when there is statistical difference observed between prior and current data
Using DP operating characteristics can be controlled by modifying parameters of discount function – no need to inflate posterior probability acceptance criteria.

## Slide 22: Mean squared error (MSE)
MSE is computed as the mean of the squared bias
The MSE of the posterior estimate decreases for all methods when the mean of the current data is near zero
As the true value moves away from zero, the MSE increases and becomes larger near and
But all methods then tend to shrink towards the standard deviation of the current data, i.e.,
DP methods converge to the standard deviation of the current data faster than the hierarchical and commensurate prior
Discordant regions
Discordant regions

## Slide 23: Power
Agreement regions
Discordant regions
0.025
Target type 1 error 0.025

## Slide 24: Summary
DP models leverage the prior similarly to the other approaches when the prior and current data are similar
When there is significant differences observed between the prior and current data only the DP model reduces the weight of the prior to a point where noninformative operating characteristics are observed.
The persistence of inflated bias, type 1 error, and MSE in the discordant regions for the other methods is concerning since there can be substantial evidence that the prior and current data come from different populations.
The DP with identity is both easy to understand has no tuning parameters and performs admirably in all cases, this is clearly a good choice unless major type 1/bias error modifications are necessary
Bayesian approach | Good Operating characteristics | Easy to explain and implement | Computational burden | Applicable to many types of trials
Discount Prior | Yes | Yes | Yes | Yes